## Slide 1: Company & Product Overview
Network Test and Emulation
<number>
  Presented by Hun-Kyi Wynn
  hkwynn@candelatech.com , www.candelatech.com
  Tel: +1 360-380-1618, Mobile: +1 360-305-6822
Notes: <number>
Put you contact information here.

## Slide 2: Company Overview
Network Test and Emulation
<number>
Established in 2000 by Ben Greear, CEO, author of Linux VLAN code.
Address a niche of affordable real world network traffic generation equipment – LANforge FIRE.
Initially, HW based but moved to COTS HW with advantages of realism.
Architecture facilitated development of network emulation equipment – LANforge ICE.
Proponents of the Open Source advantage and the value proposition for our customers.
Notes: <number>
Our low overhead and use of Open Source and COTS allows us to produce highly affordable, stable and fully featured equipment without passing unnecessary costs to the customer. Open Source and a talented technical pool allows us to tailor solutions to customers needs in a relatively short period of time. This flexibility is hard to find in other larger companies.

## Slide 3: Sales Process
Winning sales:
  LANforge is typically the most affordable option.
  Feature set is near the top of the industry.
  Currently, no other solution supports line-speed GigE and virtual-routing capabilities, in conjunction with integrated LANforge-FIRE traffic generation feature set.
  Small company means excellent tech & pre-sales support. There is only top-tier support, no bottom-tier out-sourced support staff to waste customer’s time.
  Flexible licensing that does not restrict deployment topologies, i.e. move LANforge from lab testing to field testing is not restricted.
  Able to add reasonable customer requests in timely manner, independent of road map.
Network Test and Emulation
<number>

## Slide 4: Sales Process
Notable LANforge ICE sales wins:
  Large gaming companies (Sony, THQ, Activision, Vivendi, VMC) use LANforge for online game testing, with excess of 80 concurrent emulations per system.
  Ernst & Young repeatedly buy large systems to emulate 8 concurrent high-speed emulations.
  Military & Aero-space companies: Lockheed Martin, Navy, SAIC, Raytheon, General Dynamics.
  Many other organizations: International banking, state & federal, foreign military, telecoms, etc.
Network Test and Emulation
<number>
Notes: Gaming: Sony & THQ and other smaller ones.
<number>

## Slide 5: Home Page: http://www.candelatech.com
Network Test and Emulation
<number>
Notes: <number>
Just to point out the overall organization of the home page.

## Slide 6: LANforge Links
Jul 29, 2026
Network Test and Emulation
<number>
Support Mailing List:
http://www.candelatech.com/mailman/listinfo/lanforge
Download Presentations and Datasheets:
http://www.candelatech.com/pdfs
Self Guided Training - Cookbook:
http://www.candelatech.com/lanforge_v3/lfgui_cookbook.html
Documentation and FAQ:
http://www.candelatech.com/doc.html
http://www.candelatech.com/wiki/index.php/LANforge-FAQ
Notes: 29 Jul 2026
<number>
Application slides to be added.

## Slide 7: System Architecture
Network Test and Emulation
<number>
GUI
Manager
Resource
(FIRE/ICE)
Resource
(FIRE/ICE)
Resource
(FIRE/ICE)
Resource
(FIRE/ICE)
• • •
Normally a Common Platform
LANforge
Notes: <number>
A high level schematic view to help explain the concepts behind the LANforge system.

## Slide 8: System Elements
Network Test and Emulation
<number>
The System: GUI, Manager and Resources
The GUI: Displays and records data reported by the Resource Manager. Generates control and configuration requests to the Resource Manager.
A Manager: Only one in a system that performs data collection, configuration, control, licensing and can also be a Resource.
A Resource: Network Traffic Generator (LANforge FIRE) and/or Network Emulator (LANforge ICE).
Notes: <number>
Description of the elements on the System Architecture diagram.

## Slide 9: System HW Features
Form factor support: Compact Network Appliance, Near Silent Appliance, Shuttle PC, PC, Rack Mount Server, Laptop, Rugged Portable PC. Compact form factors good for customer demos, on-site support and desktop development. Other form factors give flexibility in deployment.
Compact Network Appliance
WiFi Compact Network Appliance
1U Rackmount Appliance
Notes: Common HW feature to both LANforge FIRE and LANforge ICE that emphasize value to the customer.

## Slide 10: System HW Features
Network Test and Emulation
<number>
Interface support: 10/100/1000/10Gbe copper/fiber ethernet, 802.11a/b/g, T1/E1 and even Token Ring! Using generic interface HW allows cost effective reuse of LANforge investment.
Speed support: 10 bps to 1 Gbps FDX, +1 Gbps available. Provides an affordable broad performance envelope.
Sub-millisecond precision and accuracy attainable without the need for custom HW.
Compact Near Silent Appliance
Rugged Portable PC
Notes: <number>
Common HW feature to both LANforge FIRE and LANforge ICE that emphasize value to the customer.

## Slide 11: System SW Features
Network Test and Emulation
<number>
Standard HW support x86-32/64 allows the use of COTS HW.
Linux supported: FC28. Unofficially supported: SUSE, Debian and others. Customers can use an existing and familiar distribution to reduce the learning curve.
Windows (minus Armageddon, VLANs, Virtual-Routers, NAT, DHCP) gives flexibility in deployments for existing platforms.
Live-CD allows complete temporary installation of LANforge on any platform to increase the number of LANforge resources without additional investment in HW.
JAVA based GUI that is GPL’d enables localization and customization.
continued…
Notes: <number>
Common SW features that emphasize cost efficiency through flexibility and openness.

## Slide 12: System SW Features
Network Test and Emulation
<number>
Scriptable interface helps automate testing. Perl scripts provided free.
Automated DB backup to preserve previous test configurations.
Spreadsheets exported in standard CSV enable graphing of collected data for engineering analysis and management reports.
Multiple users can share a LANforge system thereby leveraging investment. User administration feature prevents friendly fire.
802.1q VLAN trunking support allows LANforge to be shared lab resource through network architecture.
Remote sniffing of packets from any LANforge interface for efficient debugging of problems.
Notes: <number>
More common SW features that help the customer achieve maximum return from their investment.

## Slide 13: LANforge ICE Features
Network Test and Emulation
<number>
Standard impairment control: speed, latency, jitter, loss, reorder & duplication.
Packet Corruption Control allows user to specify the corruption location within a packet, the type of corruption and the percentage of packets to be affected by the corruption.
WANpath supports MAC or IP filtering to apply impairment behaviour on specific flows.
Bridged or routed mode for easy integration into customer network architectures. Virtual routers support OSPF.
NAT and DHCP client and server emulation aids network integration and testing. NAT supports port forwarding.
continued…
Notes: <number>
In addition to the common HW and SW features here is a review of the LANforge ICE specific features.

## Slide 14: LANforge ICE Features
Network Test and Emulation
<number>
WAN Replay reproduces latency profile captured with the ICEcap tool.
ICEcap captures latency profiles in an editable XML file for replay in ICE.
Packet dump feature captures packet flows for replay in LANforge FIRE traffic generator.
LANforge ICE runs on LANforge kernels or standard Linux kernels.
WISER (Wireless IP Scalable EmulatoR) sub-system emulates mobile military wireless networks with terrain, propagation and radio impairments to IP traffic. Developed in partnership with Telcordia.
continued…
Notes: <number>
In addition to the common HW and SW features here is a review of the LANforge ICE specific features.

## Slide 15: LANforge ICE Features
Network Test and Emulation
<number>
QoS queue supported: FIFO and WRR.
Wireless collision domain emulation.
Optional simplified LANforge ICE GUI reduces user learning curve.
Virtual WiFi Access Point emulation.
Able to induce delay of 8000 ms @ GigE speed. Equivalent of 1.5 million miles or 23.35 µly (micro light-year).
Netsmith feature provides GUI for virtual network configuration and control.
Notes: <number>

## Slide 16: LANforge ICE Applications
Network Test and Emulation
<number>
Bridged
  Simplest way to integrate LANforge ICE into your network.
  Does not require any configuration changes to the network.
  Will bridge all 802.1q VLANs transparently.
LANforge ICE
Router B
Router A
Router B
Router A
Network Before
Network After
eth0
eth1
Notes: <number>
From our experience, sometimes the simplest configuration is the hardest one for customers to understand since they are expecting something more complex.

## Slide 17: LANforge ICE Applications
Network Test and Emulation
<number>
802.1q Trunking
  Allows different networks/VLANs to experience different impairments.
  LANforge ICE can be a shared resource using only two physical interfaces.
Network A
Network B
Network C
Router
L2
Ethernet
Switch
VLAN A
VLAN B
VLAN C
802.1q
Trunk
802.1q
Trunk
LANforge ICE
eth0
eth1
Notes: <number>

## Slide 18: LANforge ICE Applications
Network Test and Emulation
<number>
Routed
  Through routing LANforge ICE is able to provide multiple simulation flows as well as multiple routers. DHCP and NAT will be supported in release 5.0.3.
Network A
LANforge ICE
&
Router
Network B
Network C
eth0
eth1
eth2
T1
simulation
DS3
simulation
Satellite
simulation
Notes: <number>

## Slide 19: LANforge ICE Road Map
Network Test and Emulation
<number>
Release 5.0.7 targeted availabilty August 1, 2009:
  Increase scalability of virtual network elements.
  Optimize 10Gbe performance.
  GUI based script configuration and execution.
  Multiple Resources in Netsmith.
  Continue to simplify and improve GUI.
  WanLink optimisation to support > 1 Gbps bi-directional.
  Ubuntu LANforge LIVE CD + installer.
Notes: <number>

## Slide 20: LANforge ICE Road Map
Network Test and Emulation
<number>
Future releases:
  Application Layer ICEcap:
    Support protocols other than ICMP for more realistic profiling.
  Advanced Impairments:
    WANpath filter on port, protocol and other parameters.
    Impairments based on statistical models.
    Additional impairment types.
    Time Varying Network Impairments to help satisfy TIA-921 and ITU G.1050, e.g. bursty background traffic on emulations.
    Expand QoS emulation.
    Better support for emulation broadcast domains.
  continued…
Notes: <number>
Candela Technologies has integrated new customer features in short time frames by industry standards. We have found that we can work with our customers to achieve mutually beneficial arrangements.

## Slide 21: LANforge ICE Road Map
Network Test and Emulation
<number>
Future releases:
  Advanced Impairments:
    Replay Netflow/IPFIX Capture Characteristics.
  Support Other routing protocols BGP, RIP, etc.
  Netsmith show multiple Resources at one time.
Notes: <number>
Candela Technologies has integrated new customer features in short time frames by industry standards. We have found that we can work with our customers to achieve mutually beneficial arrangements.

## Slide 22: LANforge ICE Case Study
Network Test and Emulation
<number>
Purpose:
  Demonstrate the advanced capabilities and benefits of the LANforge ICE WAN emulator.
Notes: <number>
We are trying to convey that our products are fully featured and capable of addressing a customer’s need both technically and budgetary. We are confident that a similar solution from any of our competitors would not be able to compete on pricing. This case study is an actual customer scenario.

## Slide 23: LANforge ICE Case Study
Network Test and Emulation
<number>
Customer Problems:
  Customer suffered significant monthly expenditure maintaining live network resources (Cable and DSL modems) from local service providers to simulate networks in their online testing.
  Reproducing field problems proved virtually impossible due to differing behaviour of the local network compared to the network where the problems occurred.
  Debugging problems consumed significant resources.
  Lack of repeatable impairment profiles meant that emulated network tests were omitted from regression tests.
Notes: <number>
Basically, the customer was not using any WAN emulation and totally relying on their local service providers networks to provide the realism of live network testing. Naturally, they could never reproduce reported problems and had to guess what parameters were causing their applications to fail.

## Slide 24: LANforge ICE Case Study
Network Test and Emulation
<number>
LANforge Solution:
  Using the 802.1q VLAN feature and Linux bridging LANforge ICE emulates network topology that the customer was using for online testing.
  ICEcap allows customer to capture the field problem network impairment profile over a period of time and replay impairments in ICE.
Notes: <number>

## Slide 25: LANforge ICE Case Study
Network Test and Emulation
<number>
Benefits:
  Reduction in monthly expenditure.
  Reproducibility of local network and WAN impairments.
  Improved resolution times of field problems.
Additional Benefits:
  Database of captured network profiles for regression testing.
  Increased number of online testing resources from approximately 50 to 80 without additional HW cost.
  Multiple testers are able to configure their own impairment profiles and share the same LANforge ICE system.
  continued…
Notes: <number>
The customer reduced expenditure because they stopped maintaining the majority of their Cable and DSL connections. Since using ICE they are able to consistently apply impairments and not be reliant on whatever happens in their local service providers networks. With ICEcap they can ask their customers to capture the network impairment profile while using their application and reproduce the conditions in the online test lab. With the emulation they are now able to have more testers because ICE is able to support them. Individual testers or groups of testers are able to concentrate on reproducing a problem due to ICE being able to support multiple emulations.

## Slide 26: LANforge ICE Case Study
Network Test and Emulation
<number>
Additional Benefits:
  Regression testing.
  Reduced development cycle with partners.
  Reduced tester configuration of test consoles through DHCP.
Notes: <number>
Because now the customer implemented reproducible regression testing now their partners are able to use the same emulations in their own labs. This resulted in partners having their application pass acceptance testing first time whereas before several passes were required before an application was accepted.

## Slide 27: LANforge ICE Case Study
Network Test and Emulation
<number>
CT970-X System:
Notes: <number>

## Slide 28: LANforge ICE Case Study
Network Test and Emulation
<number>
Diagram
Notes: <number>

## Slide 29: LANforge ICE Case Study
Network Test and Emulation
<number>
Solution Diagram Detailed Description:
  LF-Bridge is a standard Linux machine supporting routing and bridging. Logically, each customer end station has a network interface on the LF-Bridge. The customer can thus group the end stations into the same broadcast domain (LAN) in whatever configuration is desired. The LF-Bridge system can route between bridge groups, so the Group A end stations can talk to each other via normal LAN broadcast and can talk to Group B through routing. All stations will talk through the LANforge-ICE system regardless of which other stations they are communicating with.
  The LANforge-ICE system can have a large number of 802.1Q VLAN interfaces. Each physical port on the LAN switch maps to a separate VLAN, and the LANforge-ICE WAN emulation is applied to specific VLANs. This allows a large number of distinct WAN emulations with a single LANforge machine.
  continued…
Notes: <number>

## Slide 30: LANforge ICE Case Study
Network Test and Emulation
<number>
Solution Diagram Detailed Description:
  The 802.1Q VLAN switch has one interface configured as an 802.1Q VLAN trunk. This port connects to LANforge. The other interfaces will be configured such that each interface is mapped to a particular VLAN. Un-tagged ethernet frames are sent to and received from the Customers End station(s).
  The Customers’ End stations speak regular ethernet and plug into the 802.1Q VLAN switch. If the LF-Bridge system is set up as a router, the end stations will use their associated bridge interface as their default gateway. The LF-Bridge can also be configured to be completely transparent. In this case, the end stations will use the existing network infrastructure connected to the LF-Bridge as the router.
  Reference: http://www.candelatech.com/images/ice_vlan_bridge.png
Notes: <number>

## Slide 31: Testimonial #1
Network Test and Emulation
<number>
Bridger Funding used LANforge ICE to test the deployment of a new network architecture. LANforge ICE exposed some problems during the test phase, when it was still possible to fix them!
"Thank you very much for this product and all of your help answering my crazy questions. This product has saved us a ton of time in testing out different scenarios and an equal if not greater amount of money from deploying a bad solution to the company!“
-- System Administrator
Notes: <number>

## Slide 32: Testimonial #2
Network Test and Emulation
<number>
AP Connections <www.apconnections.net>:
You’ve reached a quintessential point in business when your product has no service effecting issues. NetEqualizer has arrived at that point. For the last six months, no issues have surfaced. None. Any “problems” have been system-specific and surmountable, usually easily. It’s a great feeling.
We have to give credit where credit is due, and that would be to say that the recent surge in reliability is a direct result of an informal partnership with Candela Technologies.
continued…
Notes: <number>

## Slide 33: Testimonial #2 continued
Network Test and Emulation
<number>
…
As you can imagine as with all products installed in a network, reproducing subtle field issues in a test lab can be maddening. But Candela does it reliably. With their Lanforge line of equipment you can root out almost any issue in your network. It is what we use in house and the pay-off is immeasurable.
Thanks, Candela Tech; we both get bragging rights to your results.
Notes: <number>

## Slide 34: Demo: Objective
Network Test and Emulation
<number>
Illustrate basic LANforge FIRE and ICE functionality using a single appliance.
Demonstration realized by using virtual re-direct devices (http://lwn.net/Articles/130389/) which can have more advanced applications such as routable ICE WAN emulation.
Platform:
  <PUT SPECS HERE>
Notes: <number>

## Slide 35: Demo: References
Network Test and Emulation
<number>
Online: http://www.candelatech.com/doc.html
HELP button 
Symbol “>” is a mouseActionClick
Definition of Virtual Re-Direct Device:
  RDDs (Re-Direct Devices) are created and associated in pairs. Transmitting a packet on one RDD cause the other RDD to receive the packet. RDDs are presented as regular ethernet devices and have MACs, will do ARP, and other such things.
Notes: <number>

## Slide 36: Demo: UDP Cross Connect
Network Test and Emulation
<number>
LANforge FIRE
LANforge ICE
CX Name:
demo-udp-rdd
rdd1
rdd2
rdd0
rdd3
WANlink bridge
rdd1:
Name: demo-rdd-A
Test Manager: tm1
Speed: 1.544 Mbps
Jitter: 1% @ 20ms
Latency: 50ms
LossRate: 1%
IPAddress: none
rdd2:
Name: demo-rdd-B
Test Manager: tm1
Speed: 1.544 Mbps
Jitter: 0ms
Latency: 0ms
LossRate: 0%
IPAddress: none
WANlink Name:
demo-rdd
rdd0:
IPAddress: 1.1.1.1/24
Name: demo-udp-rdd-A
TXSpeed: 1.024 Mbps
PacketSize: 300 bytes
PldPattern: Increasing
rdd3:
IPAddress: 1.1.1.2/24
Name: demo-udp-rdd-B
TXSpeed: 1.024 Mbps
PacketSize: 300 bytes
PldPattern: Increasing
Notes: <number>

## Slide 37: Demo: VoIP Cross Connect
Network Test and Emulation
<number>
LANforge FIRE
LANforge ICE
CX Name:
demo-voip-rdd
rdd1
rdd2
rdd0
rdd3
WANlink bridge
WANlink Name:
demo-rdd
rdd1:
Name: demo-rdd-A
Test Manager: tm1
Speed: 1.544 Mbps
Jitter: 1% @ 20ms
Latency: 50ms
LossRate: 1%
IPAddress: none
rdd2:
Name: demo-rdd-B
Test Manager: tm1
Speed: 1.544 Mbps
Jitter: 0ms
Latency: 0ms
LossRate: 0%
IPAddress: none
Demo: VoIP Cross Connect
LANforge FIRE
LANforge ICE
CX Name:
demo-voip-rdd
rdd1
rdd2
rdd0
rdd3
WANlink bridge
WANlink Name:
demo-rdd
rdd0:
Name: demo-voip-rdd-A
Record: Enable
PESQ: Enable
Originator Only
rdd3:
Name: demo-voip-rdd-B
Record: Enable
PESQ: Enable
Terminator Only
rdd1:
Name: demo-rdd-A
Test Manager: tm1
Speed: 1.544 Mbps
Jitter: 1% @ 20ms
Latency: 50ms
LossRate: 1%
IPAddress: none
rdd2:
Name: demo-rdd-B
Test Manager: tm1
Speed: 1.544 Mbps
Jitter: 0ms
Latency: 0ms
LossRate: 0%
IPAddress: none
Cross Connect Information:
Test Manager: tm1
CX Type: SIP
Min Call Duration: 60s
Max Call Duration: 180s
CODEC: G729a
Notes: <number>

## Slide 38: Demo: Connect to LANforge
Network Test and Emulation
<number>
>Discover, >Connect
>Server Name/IP: [yourLANforge]:4002, >Connect
>Control, >Connect
Status:
Blue = Management Interface
Green = Running Resource Interface
Yellow = Phantom Resource Interface
Link State and Negotiation
Notes: <number>

## Slide 39: Demo: Create rdds
Network Test and Emulation
<number>
>Port Mgr, >Create, >Redirect, >First Redir Name: rdd0, >Second Redir Name: rdd1, >OK
>Create, >Redirect, >First Redir Name: rdd2, >Second Redir Name: rdd3, >OK
>Alias: rdd0, >Modify, >IP Address: 1.1.1.1, >IP Mask: 255.255.255.0, >OK
>Alias: rdd3, >Modify, >IP Address: 1.1.1.2, >IP Mask: 255.255.255.0, >OK
Notes: <number>

## Slide 40: Demo: Create Test Mgr
Network Test and Emulation
<number>
>Test Mgr, >Create, >Test Manager Name: tm1
>Free Clients: default_gui, >Add Client
>Free Clients: default, >Add Client
>OK
Notes: <number>

## Slide 41: Demo: Create WANlink
Network Test and Emulation
<number>
>WanLinks, >Create
>Name: demo-rdd, >Test Manager: tm1
demo-rdd-A, >Port: rdd1, >Jitter-Freq: 10000, >Transfer Rate: 1544000, >Latency: 100, >Jitter: 20, Drop-Freq: 1000, >Kernel-Mode
demo-rdd-B, >Port: rdd2, >Transfer Rate: 1544000, >Kernel-Mode
Notes: <number>

## Slide 42: Demo: Create UDP CX
Network Test and Emulation
<number>
>Layer-3, >Create
>CX Name: demo-udp-rdd, CX Type: LANforge/UDP, >Test Manager: tm1
demo-rdd-A, >Port: rdd1, >Jitter-Freq: 10000, >Transfer Rate: 1544000, >Latency: 100, >Jitter: 20, Drop-Freq: 1000, >Kernel-Mode
demo-rdd-B, >Port: rdd2, >Transfer Rate: 1544000, >Kernel-Mode
Notes: <number>

## Slide 43: Demo: Create VOIP CX
Network Test and Emulation
<number>
>VOIP/RTP, >Create
>CX Name: demo-voip-rdd, >Test Manager: tm1, >CX Type: Voice – SIP, >Min Call Duration: 60, >Max Call Duration: 180, >Codec: G729a
demo-voip-rdd-A, >Port: rdd0, >Record, >Enable PESQ
demo-voip-rdd-B, >Port: rdd3, >Record, >Enable PESQ
Notes: <number>

## Slide 44: Demo: Miscellaneous
Network Test and Emulation
<number>
Poll Mgr
Card Mgr
Notes: <number>

## Slide 45: Specifications
Network Test and Emulation
<number>
Notes: <number>

## Slide 46: Pricing
Network Test and Emulation
<number>
Notes: <number>